## Slide 1
Red Planet Recycle
An Investigation Into Advanced Life Support system for Mars
Tuesday 24th January, 2 PM
Chemical Engineering
Design Projects 4

## Slide 2
Outline
Design objectives
Stages 1 & 2 outline
Criteria & Constraints
Water treatment
Air treatment
Discussion

## Slide 3
Outline
1. Design
objectives
Design Brief
Your consulting company has been hired by the Mars Exploration Consortium, represented by Drs. Sarkisov and Valluri. The objective of the consortium is to build a space station on Mars, capable of a continuous support of a 10 member crew. It has been planned that a re-supply mission should return to Mars every 18 months, with the main resources re-supplied being water, oxygen and food. With the current cost of the re-supplement estimated at £1 M/kg, there is a clear need for intensive onsite recycling of the resources, including water, air and waste. Your company has been hired to develop an integrated recycling solution, with an objective to minimize the weight of the re-supplement cargo. Other technologies that should be explored along with the recycling, include collection and purification of water on Mars and local production of food stock (high protein vegetables etc). The primary source of energy for the Martial station will be provided by a nuclear reactor with up to 50 MWe capacity.

## Slide 4
Outline
1. Design
objectives
Design Outline
We have identified 3 key stages of the design:
Resource requirements assuming no recycling or utilisation of local sources
Resource requirements with recycling introduced
Resource requirements with recycling introduced and utilisation of local resources. Investigation into unconventional technologies

## Slide 5
Outline
1. Design
objectives
Using previous isolated systems as examples the essential resources that must be controlled in a life support system are:
Water
Air
Food
Waste
Thermal energy
Biomass
The last three require control but no resupply on the Mars space station, therefore these are not considered at this stage of design.
2. Stages
1&2 Outline
Stage 1 – Design basis

## Slide 6
Outline
1. Design
objectives
Stage 1 – Resource requirements
Total Water Requirement |  |  | 
Drinking | Hygiene* | Safety | Total
[kg] | [kg] | [kg] | [kg]
17472 | 92345 | 27454.25 | 137271.25
Total Air Requirement |  |  |  | 
N2 | O2 | CO2 | Safety | Total
[kg] | [kg] | [kg] | [kg] | [kg]
0 | 4599 | 0 | 1149.75 | 5748.75
Calorific requirement |  | 
Standard | Safety | Total
[MJ] | [MJ] | [MJ]
57.3 | 14.325 | 71.625
Total Oxygen | Total Water | Total Resupply Weight | Total Resupply Cost
[kg] | [kg] | [kg] | [£Million]
5748.75 | 137271.25 | 143020 | 143020
2. Stages
1&2 Outline

## Slide 7
Outline
1. Design
objectives
Design Outlook
Stage 1 | Stage 2 | Stage 3
2. Stages
1&2 Outline

## Slide 8
Outline
1. Design
objectives
Stage 2 – Design basis
Stage2: Introducing recycling processes to the Mars space station in order to minimise the resupply requirements
Of the three focus resources identified in stage one, only two can effectively be recycled. These are:
Water
Air
2. Stages
1&2 Outline

## Slide 9
Outline
1. Design
objectives
Water Recycling
Assumptions:
All consumed water requires recycling
Assuming NASA standard water composition
2. Stages
1&2 Outline

## Slide 10
Outline
1. Design
objectives
Water Recycling Design Basis
Stage 1
Water
Waste water
(ppm)
Treated water
(ppm)
Ammonia 55 calcium 0.9
chlorine 229 phosphate 134 sulphate 80 Nitrate <100 sodium 150 potassium 133 magnesium 1.5 TOC >11
Ammonia 0.05 calcium 30
chlorine 200 phosphate N/A sulphate 250 Nitrate 10 sodium N/A potassium 340 magnesium 50 TOC <0.5
Flowrate 200.6 kg/day
2. Stages
1&2 Outline
M.Flynn (1998)

## Slide 11: ?
Outline
1. Design
objectives
Air Recycling
Assumptions:
The air treatment is split into three distinct processes: CO2 separation, CO2 consumption and O2 production
Assuming same composition of air as on Earth
Assume N2 is a buffer
2. Stages
1&2 Outline

## Slide 12: ?
Outline
1. Design
objectives
Air Recycling Design Basis
Stage 1
Air
Pre-treatment
10 kg/day CO2
Stage 1
Air
Air treatment
8.4 kg/day O2
Air
Air
2. Stages
1&2 Outline

## Slide 13
Outline
1. Design
objectives
Criteria & Constraints
Applicability
Reliability
Modularity
Resupply
But in general we look for the technology to be;
Lightweight and economical, able to recover a high percentage of waste water and operate with minimal consumables
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 14: ?
Outline
1. Design
objectives
Criteria & Constraints- Water treatment
2. Criteria & constraints
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
4. Water
treatment
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 15: ?
Outline
1. Design
objectives
Criteria & Constraints- Water treatments
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
4. Water
treatment
2. Stages
1&2 Outline
3. Criteria &
Constraints

## Slide 16: ?
Outline
1. Design
objectives
Water treatment- Final 5
2. Criteria & constraints
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 90
Maintanence | Unknown | - | 50 days | >18 months
4. Water
treatment
3. Stages
1&2 Outline

## Slide 17: ?
Outline
1. Design
objectives
Water treatment- Final 5
2. Criteria & constraints
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 92 | - | 99 | 90
Maintanence | Unknown | - | 50 days | >18 months
4. Water
treatment
3. Stages
1&2 Outline

## Slide 18: ?
Outline
1. Design
objectives
DOC VS ISS WATER RECOVERY SYSTEM
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
DOC requires a Re-supply of 4393 kg every 18 months
ISS Water Recovery System requires a Re-supply of 1032 kg every 18 months
Due to the difference in weight per Re-supply mission we have decided to choose to design the ISS Water Recovery System. However this is based on the 2007 paper where the recovery rate of the DOC system was 96%. If a more recent paper is able to determine a greater recovery rate the DOC system should be reconsidered for design.

## Slide 19: ?
Outline
1. Design
objectives
Gas/Liquid Separator
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
The PFD shows that the stream exiting the Reactor enters the Gas/Liquid Separator before moving on to the Ion-Exchange bed.
The Stream Leaving the Reactor contains oxidized organics which need to be removed from the system.
The Separator needs to be designed to remove the excess Oxygen before the Stream continues to the IX Bed.
Excess Oxygen can be damaging and so its removal is also important for protecting expensive equipment.

## Slide 20: ?
Outline
1. Design
objectives
Methods of Removal
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
In order to determine the Method of Removal the phase and composition of the stream exiting the Reactor needs to be determined
From the PFD it is known excess oxygen needs to be removed. If the oxygen is dissolved in a liquid stream, membrane degasification is an option as it is able to remove the dissolved gas by allowing it to pass through the Gas-Liquid Separation membrane.

## Slide 21: ?
Outline
1. Design
objectives
Schematic of ISS Technology
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline

## Slide 22: ?
Outline
1. Design
objectives
ISS Urine Purification
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline

## Slide 23: ?
Outline
1. Design
objectives
Multifiltration Beds
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
MF consists of a particulate filter upstream of six unibeds in series. Each unibed is composed of an adsorption bed (activated carbon) and ion exchange resin bed.
  Particulates are removed by filtration
  Suspended organics are removed by adsorption beds
  Inorganic salts are removed by ion exchange resin beds.
  Source: Mark Kliss, NASA ARC
The MF canisters are designed for a 30 day life, and hence will be replaced on a monthly basis.

## Slide 24: ?
Outline
1. Design
objectives
Schematic of a MF Bed
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline

## Slide 25: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Media | Function | Media Description
MCV-77 | Disinfection | iodinated strong base anion, SBA, exchange resin
IRN-150 | Removal of anions and cations | mixture of gel types strong acid cation, SAC, (IRN-77, H+ form) and SBA (IRN 78,OH- form)
IRN-77 | Removal of cations | SAC gel exchange resin in the H+ form
IRA-68 | Removal of strong and weak acids | weak base anion, WBA, gel exchange resin in the free base form
580-26 | Removal of nonpolar organics | coconut-shell based activated carbon
APA | Removal of nonpolar organics | bituminous-coal based activated carbon
XAD-4 | Removal of nonpolar organics | polymeric adsorbent
IRN-150 | Removal of anions and cations | mixture of gel types SAC (IRN-77 , H+ form) and SBA (IRN-78, OH- form)
IRN-77 | Removal of cations SAC | gel exchange resin in the H+ form
Ref. David Robert Hokanson, MICHIGAN TECHNOLOGICAL UNIVERSITY

## Slide 26: ?
Outline
1. Design
objectives
Aqueous Catalytic Oxidation Reactor
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Used as an effective post-treatment technology for the removal of low molecular weight polar (but non-ionic) organics which are not removed by sorption in the multifiltration (MF) train.
Typical contaminants of this kind are ethanol, methanol, isopropanol, acetone, and urea

## Slide 27: ?
Outline
1. Design
objectives
Aqueous Catalytic Oxidation Reactor
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Design:
The reactor operating pressure is determined primarily by the requirement to maintain water in the liquid phase
The ISS uses a VRA which is co-current bubble column which uses gas phase oxygen as the oxidant over a catalyst
Catalyst consists of a noble metal on an alumina substrate
For design assume plug flow reactor

## Slide 28: ?
Outline
1. Design
objectives
Ion Exchange Bed
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Removes dissolved products of oxidation exiting the reactor
Including both organic & inorganic compounds
Organic Anion exchanged bed contains a synthetic resin, often styrene based with a capacity of 10-12 kg/ft3*
(*Nalco Chemical Company, 1998)

## Slide 29: ?
Outline
1. Design
objectives
New Proposed System
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Aim to remove volatile organic compounds (VOC) from the cabin air via catalytic oxidation prior to absorption in the aqueous phase
This reduces the load on the Ion exchange bed. Oxidation kinetics indicate this is more efficient.
Second, vapour compression distillation (VCD) technology processes the condensate and hygiene waste streams in addition to the urine waste stream

## Slide 30: ?
Outline
1. Design
objectives
New Proposed System
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
Experimental evidence (Carter et al.,2008) shows this system can effectively reduce the Total Organic Compounds (TOC) to ‘safe levels’:
TOC removal by organic reactor
Carter, et al., 2008)

## Slide 31: ?
Outline
1. Design
objectives
Questions
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
The composition and Phases of the Reactor Exit Steam?
Confirmation of what needs removed from the Reactor Exit Stream prior to it entering the Ion Exchange bed?
If a Gas-Liquid Separation Membrane is the most appropriate method of Removing Oxygen?

## Slide 32: ?
CO2 Separation
CDRA - Carbon Dioxide Removal Assembly (ISS)
PSA – Pressure Swing Adsorption
MEA CO2 Absorption
Activated Carbon Absorption
Scrubbers
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 33: ?
1. CDRA – Process Description
Utilises regenerative molecular sieve technology to remove carbon dioxide.
In the CDRA, there are four beds of two different zeolites.
Zeolite 13x absorbs water, while zeolite 5A absorbs carbon dioxide.
Each side of the CDRA contains a zeolite 13X connected to a zeolite 5A bed.
As the air passes through the zeolite 13X bed, water gets trapped and removed from the air.
The dried air goes into the zeolite 5A bed where carbon dioxide gets trapped and removed.
The outgoing air is then dry and free from carbon dioxide.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 34: ?
1. CDRA – Simplified PFD
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 35: ?
2. PSA – Process Description
Similar process to the CDRA with the exception that pressure is used instead of heat.
Beds are operated at 150kPa or higher.
Higher the pressure, the more CO2 is adsorbed.
When bed becomes saturated it is depressurised to atmospheric levels.
CO2 is released from the bed and the regeneration is complete.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 36: ?
3. MEA CO2 Absorption
This is a regenerative method of removing CO2 from air.
Uses an aqueous solution of 25-30 wt.% (4-5 M) monoethanolamine (MEA), NH2CH2CH2OH to absorb the CO2 from the air.
The aqueous solution is then regenerated by passing it through a column of packed glass rings and by heating it to drive off the CO2 under pressure. As shown below.
H-O-CH2-CH2-NH-CO-OH  H-O-CH2-CH2–NH2 +O=C=O
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 37: ?
4. Activated Carbon Adsorption
A form of carbon that has been processed to make it highly porous so as to have a very large surface area available for adsorption or chemical reactions.
CO2 saturated air is passed over the activated carbon and the CO2 is adsorbed onto the surface.
Can be regenerated by blowing air with a low CO2 concentration through the bed.
Only useful to us if we have a waste stream of air from another process that can be used to clean it.
There is no way of gaining a pure CO2 stream, which may cause problems in later processes when converting the CO2 to O2. Therefore this technology is not applicable to the space station.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 38: ?
5. Scrubbers
Soda Lime – used on submarines
Constant air circulation through a scrubber system filled with 75% calcium hydroxide. CO2 is removed via the following reaction.
CO2 + Ca(OH)2 → CaCO3 + H2O
Non regenerative, Ca(OH)2 must be resupplied.
Lithium Hydroxide – used in spacesuits
Used to remove CO2 from exhaled air by one of two reactions.
2 LiOH·H2O + CO2 → Li2CO3 + 3 H2O
2LiOH + CO2 → Li2CO3 + H2O
Second is lighter and produces less water.
Neither systems are regenerable and LiOH must be resupplied.
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 39: ?
Criteria & Constraints- CO2 Separation
Technology | Applicability | Reliability | Modularity | Resupply
CRDA |  |  |  | 
MEA Absorption |  |  |  | 
Activated Carbon |  | - | - | -
PSA |  |  |  | 
Sorbents |  |  |  | 
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 40: ?
Criteria & Constraints- CO2 Separation
Technology | Applicability | Reliability | Modularity | Resupply
CRDA |  |  |  | 
MEA Absorption |  |  |  | 
Activated Carbon |  | - | - | -
PSA |  |  |  | 
Sorbents |  |  |  | 
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 41: ?
CO2 Separation - Final 3
 | CDRA | MEA Absorption | PSA
Resupply (kg/18 months) | 0 | 0* | 0
No. of independent units | 2 | 2 | 2*
Feed streams | 1 | 1 | 1
Recovery rate (%) | - | 70-90 | 95*
Maintenance (years) | 3-5 | - | 3-5
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 42: ?
CO2 Separation - Final 3
 | CDRA | MEA Absorption | PSA
Resupply (kg/18 months) | 0 | 0* | 0
No. of independent units | 2 | 2 | 2*
Feed streams | 1 | 1 | 1
Recovery rate (%) | - | 70-90 | 95*
Maintenance (years) | 3-5 | - | 3-5
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment

## Slide 43: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 Separation
Temperature swing adsorption with molecular sieves.
  Temperature swing versus pressure swing.
  Zeolites preferred to activated carbon for the adsorbent.
  How the ISS system operates
  Differences between the ISS system and that which we will design
  Mass balance
  Design requirements

## Slide 44: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
TSA
Advantages:
  Can achieve higher product purities than PSA in low CO2 environments
  Cheaper than PSA
Indirect heating
  Direct heating requires large volumes of adsorbent and high heating requirements.
  An intercoaxial heat exchanger can solve this problem
  Water circulation to provide a heat sink during adsorption
  Steam condensation to provide heat for desorption

## Slide 45: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Choice of Adsorbent
Activated Carbon or Molecular Sieves?
A comparison of activated carbon to two molecular sieves (13X and 4A) showed preferential adsorption of CO2 over nitrogen or hydrogen at all pressures up to 250 psia.
13X and 4A performed better than activated carbon at low pressures, but activated carbon was preferential at high pressures.
Our system will operate at a low (atmospheric) pressure – indicates molecular sieves are a preferential choice.
No data could be found on how activated carbon and molecular sieves act at different temperatures but all examples of TSA systems used molecular sieves – it is a proven and preferred technology.

## Slide 46: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CDRA - ISS

## Slide 47: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CDRA - ISS
There are a few main differences between that system and ours that should be considered.
Larger crew – capacity of system should be higher.
CO2 must be recycled – on ISS the stream is vented into space and uses the vacuum outside the vessel to desorb the CO2 and vent it. An alternative system for desorption is needed.

## Slide 48: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Mass Balance
0.416667 kg/hr CO2 produced by crew members.
Assuming composition of air inside the station is 20.95% O2, 0.03% CO2, and the remainder (79.02%) N2.
Due to the 95% CO2 removal rate 161.95 kg/hr of cabin air needs to be treated.

## Slide 49: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Mass Balance

## Slide 50: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Design Requirements
2 x Dessicant bed for water removal
2 x Adsorbent bed for CO2 adsorption
Pre-cooler
Vacuum system to remove the desorbed CO2
Intercoaxial HE
Humidity control system (Plate heat exchanger)

## Slide 51: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 Treatment
RWGS
Sabatier
Bosch
Bosch-Boudouard

## Slide 52: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- CO2 treatment
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 

## Slide 53: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- CO2 treatment
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 

## Slide 54: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
 | Sabatier | RWGS
Resupply (kg/18 months) | 2343.5 | 1334.2
No. of independent units | 1 | 1
Feed streams | 2 | 2
Maintanence | Unknown | Unknown
CO2 treatment – Final Two

## Slide 55: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 treatment
Feasibility studies for CO2 treatment methods indicate that the Sabatier reaction is the best choice for “stage 2”.
Possibility of improving the process in “stage 3” by recovering hydrogen from the methane, as opposed to venting it to Mars. This would create a closed loop for both H2 and O2, meaning neither would need to be resupplied.

## Slide 56: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 treatment

## Slide 57: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 treatment
A MATLAB model was used to design the Sabatier reactor. The file is currently unfinished, as it only provides an isothermal model of the reactor.
By next week, we aim to have a complete non-isothermal model.
This model will allow us to choose values for the operating pressure and temperature of the reactor.
The programme will output a residence time which will be used to establish the dimensions of the Sabatier reactor.

## Slide 58: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
CO2 treatment
Next steps:
Create a non-isothermal model of the Sabatier reactor and decide on values for operating T&P.
Find dimensions for the reactor.
Begin to design a cooling system for the reactor (essentially a double pipe heat exchanger).
Consider which type of heat exchanger should be used to heat the inlet CO2 and H2 to the desired temperature (not yet known).

## Slide 59: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Molar Flowrate vs Residence Time

## Slide 60: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Molar Flowrate vs Reactor Volume

## Slide 61: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis
Photocatalytic splitting
Thermolysis
Thermochemical cycles
Catalysis

## Slide 62: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Photocatalytic splitting
Advantages – simplicity (use catalyst suspended in water to electrolyse solution in the presence of sunlight)
Disadvantages – Critical system would depend on the availability of sufficient insolation
2. Thermolysis
Advantages - Can use methane as a fuel (if Sabatier is used)
Disadvantages – Extremely high temperatures (2000°C) required to split water which means high rate of component failure.

## Slide 63: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
3. Thermochemical Cycles
Advantages – Relatively low temperature (530°C for Cu-Cl cycle).
Disadvantages – Requires several different reactors and chlorine gas may be produced which is a potential problem.
4. Catalysis (Milstein 3 stage process).
Advantages – Low temperature (100°C) and fairly simple system, can be scaled up.
Disadvantages – Relatively new technology, may require more research before it is a viable alternative to electrolysis.

## Slide 64: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Alternatives to Electrolysis Cont…
5. Bipolar Electrolysis
Advantages – Developed from monopolar electrolyzer. Low energy consumption and high efficiency make it suitable to scale up.
Disadvantages – Compact conformation of this system lead to difficulty of initial design.
6. Laser
Advantages – Similar to photocatalystic splitting, use laser instead of sunlight, simplicity structure, can be used on Mars.
Disadvantages – Sensitive plant, low reliability and difficult to repair by astronauts. High Energy consumption.

## Slide 65: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Alternatives to Electrolysis Cont…
Alternatives to Electrolysis Cont…
7. PEM Electrolyzer
Advantages – no electrolyte required in this system, high efficiency and reliability
Disadvantages – The materials of the anode and cathode are very expensive and cannot be scaled up
8. Solid Oxide Electrolyzer
Advantages - High efficiency, exhaust heat can be recycled to save energy.
Disadvantages –High operating temperatures (Over 1000°C) lead to low system reliability. Strong limitation on cell material

## Slide 66: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Criteria & Constraints- Alternatives to Electrolysis
Technology | Applicability | Reliability | Modularity | Resupply
Photocatalytic |  | - | - | -
Thermolysis |  | - | - | -
Thermochemical Cycles |  | ? |  | 
Catalysis |  | ? |  | 
Laser |  | - | - | -
Bipolar Electrolysis |  |  |  | 
PEM Electrolyzer |  | - | - | -
Solid Oxide Electrolyzer |  | - | - | -

## Slide 67: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Oxygen Generation using Electrolysis
Design Basis
Stage 1
Air
Pre-treatment
10 kg/day CO2
Stage 2
Air
Air treatment
8.4 kg/day O2
Air
Air

## Slide 68: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Process Description
PRE-INVESTIGATION OF WATER ELECTROLYSIS
http://www.futureenergies.com/pictures/fuelcellpower.jpg

## Slide 69: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Process Description
OH- (aq) anions are oxidised at the anode, producing O2(g), H2O (l) and electrons.
The electrons flow through the diaphragm to the cathode.
At the cathode, water is reduced producing H2(g) and OH- anions (aq).
These hydroxide anions flow to the anode, where the cycle is repeated.
Modeling of advanced alkaline electrolyzers: a system
simulation approach

## Slide 70: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Process BFD

## Slide 71: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Overall Mass Balance
Assumptions
80% Conversion of H2O
All electrolyte is recycled
All un-reacted water is separated and recycled
No deterioration of electrodes

## Slide 72: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Overall Mass Balance
 |  |  |  |  | Recycle |  |  |  |  |  | 
 |  |  |  |  | 2.36 kg/day |  |  |  |  |  | 
 |  |  |  | Electrolysis Unit |  |  |  |  |  | H2 | 
 | H20 |  |  |  |  |  |  |  |  | 1.05 kg/day | 
 | 9.45 kg/day |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | O2 | 
 |  |  |  |  |  |  |  |  |  | 8.4 kg/day | 

## Slide 73: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Key Process Parameters
Voltage and Current Levels
Electrode Surface Area
System Temperature
Diaphragm Material
Electrolyte Choice
Electrode Choice

## Slide 74: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Voltage and Current Levels
Using an electrochemical basis the rate of oxygen production is related to voltage and current levels by;
With F in mol/sec

## Slide 75: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Electrode Surface Area
Faradays Efficiency is dependant upon the electrode surface area
The equation for faradays efficiency is;
This model uses non-temperature dependant coefficients

## Slide 76: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
System Temperature
Typically operated at 70-90˚C
Higher temperatures beneficial as they reduce the ohmic resistance of the electrolyte solution and that of the electrodes.
Hydrogen and Fuel Cells: Fundamentals, Technologies and Applications

## Slide 77: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Diaphragm Choice – Inorganic and Organic Materials
Important properties for choice:
Reliability / overall lifespan
Efficiency
Low electrolyte resistance
Health hazard

## Slide 78: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Inorganic - Asbestos
Being phased out of use in industries (<20% in EU)
Not suitable at higher temperatures
Corrodes/deteriorates when used alone.
Possible health problems – rule out

## Slide 79: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Refractory-Type Materials
Inorganic material combined with binder or alone.
e.g. Ceria (CeO) or zirconia E fibre.
  Both exhibit high stability.
Made into membranes by NASA.
Combined and alone yielded poor results.
  Fragile, brittle, poor strength…

## Slide 80: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Polyantimonic Acid (PAM)
Extremely stable at high temp (up to 150oC)
Stable in highly concentrated KOH
Best option: Polyarylethersulfone-PAM
  Membrane resistance 0.2cm2 at 90oC
  Reasonably easy to reproduce
Needs further testing

## Slide 81: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Sintered Nickel
Highly resistant to corrosion
Tested at 30% KOH, 50 bar and temp >150
Gives good ionic conductivity
High electronic conductivity – problem
High cost - $1000 per m2. Not a problem.
Possibly coat with oxide.

## Slide 82: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Comparison of Inorganic Materials
Material | Reliability/ Lifespan | Health Hazard | Efficiency | Low Electrolytic Resistance
Asbestos |  |  | - | -
Refractory Type |  | - | - | -
Polyantimonic Acid (PAM) |  |  | - | 
Sintered Nickel |  |  | - | 

## Slide 83: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Polybenzimidazole fibres
They are not readily attacked by oxidizing agents and have high melting points and excellent stabilities at high temperatures
It lose 80% of its tensile-strength after one month's exposure to 30 % KOH at 80 °C
Teflon
It has excellent chemical and heat resistance to alkaline media.
It is lack of wettability, bubble will occur on the surface of membrane, lead to the conductivity decreasing. Grafting techniques seem more difficult to use and have yet to be proven for the electrolyser application.

## Slide 84: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Polysulphones
It was tested at 150 °C in KOH/O2 and KOH/H2 environments, no loss of tensile strength when KOH occupy more than 70% of the solution
Maximum service temperatures in water electrolyzers are smaller than expected. Hydrophobicity lead to low conductivity
Ryton
Excellent thermal and oxidative stability, it is stable in alkaline environments even at high temperatures and high concentration of alkaline
Ryton is not widely used due to production problems

## Slide 85: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Ion-exchange membranes
Only certain ions can pass the membrane due to its high selectivity. Simplify the separation process
More instable than other materials even in low temperature. Nafion is more stable but limited to low alkaline concentration

## Slide 86: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Comparison of Organic Materials
Material | Reliability/ Lifespan | Health Hazard | Efficiency | Low Electrolytic Resistance
Polybenzimidazole fibres |  |  | - | -
Teflon |  |  | - | 
Polysulphones |  |  | - | 
Ryton |  |  | - | 
Ion-exchange membranes |  |  | - | 

## Slide 87: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Conclusion
The choice is between Sintered Nickel and Ryton.
Sintered Nickel (or other porous metal diaphragms) is the preferred choice.
This is because organic materials are generally used for electrical insulation.
We desire a low resistance to the electrolyte to avoid prohibiting the ion pathway.

## Slide 88: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Electrolyte Solution
Products of Anode
If the anode is active electrode (metal which is more active than Ag), anode will be dissolved.
If the anode is non-active electrode (Pt or Au)
According to priority of positive ions discharge:
S2- > I- > Br- > Cl- >OH-
Products of Cathode
According to priority of negative ions discharge:
K+ < Ca2+ < Na+ < Mg2+ < Al3+ < H+ < Zn2+ < Fe2+

## Slide 89: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Electrolyte Solution
Ions in the solution
Positive Ions: K+, H+
Negative Ion: OH-
Anode：
Cathode：

## Slide 90: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Electrolyte Solution
The number of electrons lost from anode is equal to the number of electrons of cathode obtained
Ideally, the concentration of KOH is a constant or accumulated as new KOH comes in.
In practice, a small part of KOH will be carried out of system by oxygen and hydrogen

## Slide 91: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Electrolyte Choice for Electrolysis
Considerations:
High resistance to corrosion, erosion, wear.
Electrical conductivity.
Suitability to situation.
Physical Properties (mass, strength).
Cost- relatively low.

## Slide 92: ?
Outline
1. Design
objectives
2. Criteria & constraints
4. Water
treatment
3. Stages
1&2 Outline
5. Air
treatment
Materials Considered
Material | Resistances | Electrical Conductivity | Suitability | Notables
Copper |  |  |  | Oxides readily.
Brass |  |  |  | <Resistant than Cu.
Graphite |  |  |  | All round usage.
Titanium |  |  |  | Lightweight.
Silver |  |  |  | Soft. Need Alloy.
Platinum |  |  |  | Doesn’t oxidse.